## Slide 1: Microarchitectural Side-Channel Attacks Part 2
Yuval Yarom
The University of Adelaide and Data61

## Slide 2: X86 L1 Cache
Tag
Set
Offset
0
6 5
12 11
 |  |  | Tag, Data
Sets
Ways
Stores fixed-size (64B) lines
Arranged as multiple (64) sets, each consisting of multiple (8) ways.
Each memory line maps to a single cache set
    Bits 6-11 select the set
    Can be cached in any of the ways in the set

## Slide 3: X86 L1 Cache
Better visualised when the cache is rotated
Memory
Cache
Sets
Ways

## Slide 4: Prime+Probe [OST05, Per05]
Attacker chooses a cache-sized memory buffer
Attacker accesses all the lines in the buffer, filling the cache with its data
Victim executes, evicting some of the attackers lines from the cache
Attacker measures the time to access the buffer
  Accesses to cached lines is faster than to evicted lines
Memory
Cache

## Slide 5: The gritty details
The observer effect
  Our code uses the cache - want to minimise our footprint
The optimising compiler removes what it thinks is dead code
  Not optimising increases the code's footprint
  Solution:
    Know your optimiser
    Use assembly language

## Slide 6: Thrashing
The cache uses a Pseudo-LRU replacement
Our probe + victim access can cause thrashing
Solution [TOS10]: Zig-zag on data
S0
S1
S2
S3
S4
S5
S6
S7
V0
S0
S1
S6
S7

## Slide 7: Hardware prefetcher
Aims to improve temporal locality
Brings data to the cache before it is required
  We do not want that!!!
Solution [TOS10]: pointer chasing
  [Per05] uses data dependency for achieving the same result

## Slide 8: Data streams
The cache aims to predict regular access patterns with fixed strides
Linear access within a page may trigger the mechanism
Solution [OST10]: Randomise order of probed sets

## Slide 9: Putting it all together
L1-capture
With L1-rattle
With rungnupg

## Slide 10: Challenges to last-level cache attacks
Difficulty in finding memory lines that map to a given cache set
  Virtual memory
  LLC slices
Large cache size and longer cache access times mean LLC Prime+Probe is very slow
Visibility of the victim memory access at the LLC
  Intel inclusive cache takes care of the issue

## Slide 11: Virtual vs. Physical addresses
In L1, the cache stride is the same as the page size (4KiB)
  The cache set is completely determined by the page offset
Phys. Memory
Cache
Virt. addresses
?

## Slide 12: Addressing uncertainty
Phys. Memory
Cache
Virt. addresses
In larger caches, the stride is bigger. Pages only contain lines of some of the cache sets.
Parts of the mapping of memory to cache sets is masked by the virtual address.

## Slide 13: Address fields
Tag
Set
Offset
0
6 5
12 11
L1 Cache
Page number
Page offset
0
12 11
Virtual address
Tag
Set
Offset
0
6 5
17 16
LLC SandyBridge
Tag
Set
Offset
0
6 5
16 15
LLC Skylake

## Slide 14: Addressing uncertainty
Phys. Memory
Cache
Virt. addresses
The attacker cannot guarantee an even cover of the cache.
Self-contention
Missed victim access

## Slide 15: Solution : Use large pages [LYG+15,IES15]
Tag
Set
Offset
0
6 5
12 11
L1 Cache
Page number
Page offset
0
12 11
Virtual address
Tag
Set
Offset
0
6 5
17 16
LLC SandyBridge
Tag
Set
Offset
0
6 5
16 15
LLC Skylake
A feature of the MMU. Large pages (2MiB or bigger) reduce the overhead of address translation
Large page number
Large page offset
0
21 20
Virtual address

## Slide 16: Solution – large pages
Phys. Memory
Cache
Virt. addresses

## Slide 17: Intel LLC Slices
The last-level cache is divided into slices
One slice per core
  Two in Skylake?
The slice for a memory line is chosen using an undisclosed hash function
Tag
Set
Offset
0
6 5
17 16
LLC SandyBridge
Hash

## Slide 18: Reverse Engineering the Hash Function
[MLN+15] Use performance counters to RE linear hash functions (number of cores is a power of two)

## Slide 19: Reverse Engineering the Hash Function
[YGL+15] use timing to RE the function for 6 cores

## Slide 20: Reverse Engineering the Hash Function
[MLN+15] Use performance counters to RE linear hash functions (number of cores is a power of two)
[YGL+15] use timing to RE the function for 6 cores
But – need physical addresses
  Can be done on Linux < 4.0
  Unless running in a VM

## Slide 21: Probing the hash function
Start with a set of potentially conflicting memory lines
  At least twice as many as the totalsize of the cache sets
Expand a subset until it conflicts on a single set in a single slice
Contract the subset until it contains only lines of the conflicted set
Collect all of the lines of the conflicting set from the original set
Repeat until the original set is (almost) empty

## Slide 22: Expand
  Start from an empty subset
  Iteratively add lines to the subset as long as there is no self-eviction
  Self-eviction is detected by priming a potential new member, accessing the current subset and timing another access to the potential new member
🙂
🙂
🙂
🙂
🙂
🤔
😡
😈

## Slide 23: Contract
  Iteratively remove lines from the subset checking for self-eviction
  Only keep members if self-eviction disappears when removed
🙂
🙂
🙂
🙂
🙂
🤔
😈

## Slide 24: Collect
  Scan original set, looking for members that conflict with the contracted subset
🙂
🙂
🙂
🙂
🙂
🙂
🙂
😇
😇
😇
😇
😇
😇
😍
😍
😍
😍
😍
😍
😍
😍
🤕
🤕
🤕
🤕
🤕

## Slide 25: Demo
L3-capture
L3-capturecount

## Slide 26: Slow LLC Prime+Probe times
L1 (32KB) probe:
  64 sets * 8 ways *4 cycles = 2,048 cycles
Small last-level cache (6MB):
  8,192 sets * 12 ways * ~30 cycles = ~3,000,000 cycles
We cannot probe the entire LLC in a reasonable time, but probing one cache set is fast
Our solution:
  Probe one or a few cache sets at a time
  Look for temporal patterns rather than spatial footprints

## Slide 27: Demo
L3-scan

## Slide 28: Countermeasures
Hardware
System
Software

## Slide 29: Hardware countermeasure
Don't share
Hardware cache partitioning [DJL+12]
  Intel Cache Allocation Technology
Cache Randomisation [WL06]

## Slide 30: System Countermeasures
Limited sharing
  Don't share memory
  Don’t share cores
Cache Colouring [BLRB94,SSCZ11]
  STEALTHMEM [KPM12]
CATalyst [LGY+16]
CacheBar [ZRZ16]

## Slide 31: Software Countermeasures
Constant-time programming
  No variable-time instructions
  No secret-dependent flow control
  No secret-dependent memory access

## Slide 32: Non constant-time [YB14]

## Slide 33: Constant-time

## Slide 34: Constant-time

## Slide 35: Bibliography
[ABF+15] T. Allan, B. B. Brumley, K. Falkner, J. van de Pol and Y. Yarom, "Amplifying Side Channels Through Performance Degradation", ePrint 2015/1141
[AK09] O. Acıiçmez, Ç. K. Koç, "Microarchitectural Attacks and Countermeasures," in Ç. K. Koç, ed. Cryptographic Engineering, Springer US, 2009
[AS07] O. Acıiçmez and J-P Seifert, "Cheap Hardware Parallelism Implies Cheap Security", FDTC 2007
[Ber05] D. J. Bernstein, "Cache-timing attacks on AES", http://cr.yp.to/antiforgery/cachetiming-20050414.pdf, 2005
[DJL+12] L. Domnister, A. Jaleel, J, Loew, N. Abu-Ghazaleh and D. Ponomarev, "Non-Monopolizable Caches: Low-Complexity Mitigation of Cache Side Channel Attacks", TACO 8(4), 2012
[GBK11] D. Gullasch, E. Bangerter and S. Krenn, "Cache Games -- Bringing Access-Based Cache Attacks on {AES} to Practice", IEEE S&P 2011
[GYCH16] Q. Ge, Y. Yarom, D. Cock and G. Heiser, "A Survey of Microarchitectural Timing Attacks and Countermeasures on Contemporary Hardware", ePrint 2016/613
[GMWM16] D. Gruss, C. Maurice, K. Wagner and S. Mangard, "Flush+Flush: A Fast and Stealthy Cache Attack", DIMVA 2016
[GSM15] D. Gruss , R. Spreitzer and S. Mangard, "Cache Template Attacks: Automating Attacks on Inclusive Last-Level Caches", USENIX Security 2015
[IES15] G. Irazoqui, T. Eisenbarth and B. Sunar, "S$A: A Shared Cache Attack that Works Across Cores and Defies VM Sandboxing – and its Application to AES", IEEE S&P 2015.
[IES16] G. Irazoqui, T. Eisenbarth and B. Sunar, "Cross processor cache attacks", AsiaCCS 2016
[IIES14] G. Irazoqui, M. S. Inci, T. Eisenberth and B. Sunar, "Wait a minute! A fast, Cross-VM Attack on AES", RAID 2014
[Lam73] B. W. Lampson, "A Note on the Confinement Problem", CACM 16(10), 1973
[LYG+15] F. Liu, Y. Yarom, Q. Ge, G. Heiser and R. B. Lee, "Last-Level Cache Side-Channel Attacks are Practical", , IEEE S&P 2015
[MLN+15] C. Maurice, N. Le Scourance, C. Neumann, O. Heen and A. Francillon, "Reverse Engineering Intel Last-Level Cache Complex Addressing Using Performance Counters", RAID 2015
[NS16] M. Neve and J-P Seifert, "Advances on access-driven cache attacks on AES," 13th SAC, 2006

## Slide 36: Bibliography
[OST06] D. A. Osvik, A. Shamir and E. Tromer, "Cache Attacks and Countermeasures: The Case of AES", CT-RSA 2006
[pag02] D. Page, "Theoretical Use of Cache Memory as a Cryptanalytic Side-Channel," ePrint 2002/169
[Pag03] D. Page, "Defending against cache-based side-channel attacks," Information Security Technical Report, 8(1), 2003
[Per05] C. Percival, "Cache Missing for Fun and Profit", BSDCan, 2005
[PGM+16] P. Pessl, D. Gruss, C. Maurice, M. Schwarz and S. Mangard, "DRAMA: Exploiting DRAM Addressing for Cross-CPU Attacks", USENIX Security 2016
[TOS10] E. Trome, D. A. Osvik, A. Shamir, "Efficient Cache Attacks on AES, and Countermeasures", JoC 23(1), 2010
[TTMM02] Y. Tsunoo, E. Tsujihara, K. Minematsu and H. Miyauchi, "Cryptanalysis of Block Ciphers Implemented on Computers with Cache", International Symposium on Information Theory and Its Applications, Oct. 2002.
[WL06] Z. Wang and R. B. Lee, "Covert and Side Channels Due to Processor Architecture", ACSAC 2006
[WS12] Y. Wang and G. E. Suh, "Efficient timing channel protection for on-chip networks", NoCS 2012.
[WXW12] Z. Wu, Z. Xu and H. Wang, "Whispers in the Hyper-space: High-speed Covert Channel Attacks in the Cloud", USENIX Security 2012
[YB14] Y. Yarom and N. Benger, "Recovering OpenSSL ECDSA Nonces Using the FLUSH+RELOAD Cache Side-channel Attack", ePrint 2014/140
[YF14] Y. Yarom and K. Falkner, "FLUSH+RELOAD: a High Resolution, Low Noise, L3 Cache Side-Channel Attack", USENIX Security 2014
[YGH16] Y. Yarom, D. Genkin and N. Heninger, "CacheBleed: A Timing Attack on OpenSSL Constant Time RSA", CHES 2016
[YGL+15] Y. Yarom, Q. Ge, F. Liu, R.B. Lee and G. Heiser, "Mapping the Intel Last-Level Cache", ePrint 2015/905
[ZXZ16] X. Zhang, Y. Xiao and Y. Zhang "Return-Oriented Flush-Reload Side Channels on ARM and Their Implications for Android Devices", CCS 2016